### The partitioning of alkylphenolic surfactants and polybrominated diphenyl ether flame retardants in activated sludge batch tests

##### ‡Katherine H Langford, ‡Mark D Scrimshaw, †Jason W Birkett and *‡John N Lester

‡Environmental Processes and Water Technology Group,

Department of Environmental Science and Technology,

Faculty of Life Sciences,

Imperial College London,

London,

## SW7 2AZ

##### †University of Lincoln

Department of Biological Sciences

Faculty of Health and Life Sciences

Brayford Pool

Lincoln

LN6 7TS

*Corresponding author Prof. John N. Lester

Email: j.lester@imperial.ac.uk

Fax: 0207 5946016

Abstract

Polybrominated diphenyl ethers and nonylphenol polyethoxylates have been reported to be estrogenic and may enter the aquatic environment through the discharge of treated sewage effluent. Therefore, their fate during wastewater treatment processes is an important factor in determining their environmental impact. Batch tests with activated sludge from a Husmann apparatus were used to determine the effects of physico-chemical properties and sludge characteristics on the partitioning of polybrominated diphenyl ether flame retardants and nonylphenol polyethoxylate surfactants during biological wastewater treatment. Hydrophobic compounds, those with high log Kow values, were sorbed more rapidly and to a greater extent to the solid phase than more soluble compounds. For these hydrophobic compounds sorption may become an increasingly important removal mechanism as sludge age and therefore solids content increase. The initial rate of partitioning was greatest for the most hydrophobic compounds but all rates diminished with time as a result of progressive saturation of sorbent binding sites, a reduction of sorbate availability and as a consequence of the system reaching equilibrium. The sorption of polybrominated diphenyl ethers fit Freundlich adsorption isotherms demonstrating generally increasing adsorption capacity and efficiency with increasing hydrophobic nature. A correlation between increasing log Kow and increasing organic matter content was also observed for both polybrominated diphenyl ethers and nonylphenol polyethoxylates indicating the organic content of mixed liquor will also be influential in removing compounds during wastewater treatment.

Keywords

Wastewater, sludge age, log Kow, Freundlich isotherms.

1. Introduction

Polybrominated diphenyl ethers (PBDEs) are a family of flame retardants used extensively in plastics, textiles and furnishing foam to reduce fire hazards. The global production of PBDEs in 1999 was approximately 700 000 tonnes (Langford and Lester, 2002), with the global demand reported to be rising at a rate of 3-6% per year.

The PBDE flame retardants are of considerable concern because of their adverse effects on wildlife due to their endocrine disrupting properties (Meerts et al., 2000), which is of concern for higher trophic levels due to their  bioaccumulation potential (Gustafsson et al., 1999). The PBDEs are halogenated compounds, their chemical properties are similar to polychlorinated biphenyls (PCBs), with log Kow values in the range 5 to 10. Akin to the PCBs, the PBDEs have been found in a range of sediment and biological samples (Law et al., 2002) and it is likely their environmental distribution will be similar to PCBs. There has to date been very little information available on the fate of PBDEs in wastewater treatment, however similarities to PCBs indicate that they may be removed through sorption to the solid phase (Garcia-Gutierrez et al., 1982; McIntyre et al., 1981; Rahman et al, 2001).

In terms of occurrence in wastewater treatment and estrogenic activity, alkylphenol polyethoxylates (APEOs) are another significant group of compounds. There are no known natural sources of nonylphenol (NP) and nonylphenol polyethoxylates (NPEO), anthropogenic activity is the cause of their ubiquitous occurrence in the environment. Approximately 650 000 tonnes of APEO surfactants are manufactured worldwide annually (Guenther et al., 2002), and used in industry as detergents, dispersants and emulsifiers. A large proportion of these formulations are finally discharged through sewage treatment works (STW). Due to the high concentrations detected in wastewater influents and effluents, APEO removal pathways are of increasing concern particularly as the breakdown of APEO compounds results in the formation of shorter chain APEO compounds and alkylphenols (AP) which have enhanced estrogenicity (Desbrow, 1998; Routledge and Sumpter, 1996). APEO removal is dependent on degradative and sorptive processes influenced by the degree of ethoxylation. The breakdown products detected are more hydrophobic in nature and likely to sorb to the sludge or suspended solids, however, any long chained NPEOs with hydrophilic properties are more likely to be present in effluent and enter the aquatic environment where further degradation to the more actively endocrine disrupting products may occur. Low log Kow values indicate that degradation might be the most important removal mechanism for long chain NPEO compounds. However, for short chain compounds with high log Kow values, such as NP with a value of 4.8 (Ahel and Giger, 1993), sorption to the biological floc may be an important mechanism of removal.

Synthetic compounds are removed from waste streams during wastewater treatment by either biological or chemical degradation, sorption to the biological floc or volatilization (Meakins, et al., 1994). The extent of the removal of a compound has been demonstrated to be dependent on the physico-chemical properties of the compound. The properties of a compound which determine fate are aqueous solubility, organic carbon/water partition coefficient (Koc), octanol/water partition coefficient (Kow) and Henry’s Law constant (Hc). For the compounds in this study, these values are included in Table 1.

An understanding of the partitioning behaviour between the solid and aqueous phase is essential to determine the fate of a compound in STW, and is of increasing importance as concerns over their possible environmental effects escalate. It is also a critical point for both the protection of the aquatic environment, and potable supply in those areas where water re-use is practiced are STW (Gomes and Lester, 2002).

This study compares the partitioning of two groups of compounds with different physico-chemical properties and looks at their possible fate in relation to these properties. The objective was to determine if process variables such as sludge age ((c) would allow for increasing removal rates during activated sludge treatment and the implications of sorption are discussed.

2. Materials And Methods

Standards of nonylphenol (NP) and a commercial nonylphenol polyethoxylate (NPEO) mixture, Igepal CO520, were obtained from Sigma-Aldrich (Gillingham, UK). The commercial OcBDE (octa) formulation (Great Lakes DE-79) was donated by Colin Allchin (CEFAS, Burnham-on-Crouch, UK) and decabrominated diphenyl ether (DeBDE) was purchased from Lancaster chemicals (Morecambe, UK). Commercial formulations were used to represent realistic environmental concentrations, which involves commercial mixtures entering STW via influent streams. Other PBDE standards were obtained from LGC Promochem  (Hatfield, UK). All solvents used were obtained from Rathburn Chemicals Ltd (Walkerburn, UK).

Stock standards of DE-79 and DeBDE were made up in dichloromethane (DCM) and warm toluene respectively. Serial dilution into hexane followed by dilution in acetone resulted in standards suitable for spiking. DE-79 contains BDE-153 and 154 (hexa congeners) and BDE-183 (hepta congener), and three unidentified octa-BDE congeners (referred to as octa 1, octa 2 and octa 3 in this study). Igepal 520 is a commercial nonylphenol polyethoxylate mixture with an average of 5 ethoxy groups, this compound and NP stock standards were made up in acetonitrile (ACN) and diluted into 50/50 ACN/water for spiking.

2.1 Activated Sludge Samples

Activated sludge was obtained from the aeration chamber of a Husmann apparatus supplied with a synthetic settled sewage based on bacterial peptone. It was operated in a controlled temperature room at 16 oC ± 0.5, at a constant sludge age ((c) of 5 days with a DO of 3.5 mg l-1. Effluent suspended solids were typically 35–45 mg l-1 and BOD of the effluent was 20-30 mg l-1 indicative of 85% BOD removal (Stoveland and Lester, 1980). Calculation of MLSS and mixed liquor volatile suspended solids for organic carbon content (MLVSS) followed the HMSO official gravimetric method (HMSO, 1984).

The MLSS samples were refrigerated before spiking until a temperature of 4 oC was reached to minimise biological activity, then inoculated with solutions of alkylphenolic compounds or PBDEs at 0.3 mg l-1 in separate experiments. Blanks were inoculated with the respective solvents and all results were corrected for blank contamination. Duplicate samples were then taken at intervals and between sampling the MLSS was kept at 4 oC. Samples for initial partitioning work were allowed to equilibrate for 10 minutes before removal of sample aliquots.

2.2 Calculating Partition Coefficients

Partition coefficients were calculated using equations used by Dobbs et al. (1989) and Freundlich isotherms were used to calculate adsorption constants and adsorption efficiency (Gao et al., 1998).

2.3 Analysis

Robust methods for the determination of both groups of compounds were developed (Langford et al., 2004) following a review of approaches utilised by other workers (Scrimshaw et al., 2004). Alkylphenolic compounds and PBDEs were extracted separately as outlined in Fig. 1. The method for PBDE extraction and analysis was modified from those previously reported (Allchin et al., 1999; Öberg et al., 2002), NP and NPEO methods were also modified from previously reported studies  (Blackburn and Waldock, 1995; Ferguson et al., 2000; Shang et al., 1999). Recoveries achieved for NP and NPEO oligomers had an average of 82% and PBDE recoveries had a average of 95%.

LC/MS analysis was used for NP and NPEO determination using a Perkin Elmer series 200 LC coupled to a Perkin Elmer Sciex API 150 EX with a TurboIonSpray interface. A Hypersil ODS C18 (100 x 2.1 mm, 5 (m) column (Phenomenex, UK) was used and a 10 (l sample injection volume with ultrapure water to ACN gradient elution. NPEOs were detected as [M+Na]+ ions and NP as [M-H]- ions at 350 oC. The TurboIonSpray was at 3500 V and –3500 V respectively (Table 2).

PBDE determination was by GC-ECD (Perkin Elmer Autosystem XL) and GC/MS (Perkin Elmer Autosystem XL coupled to a Perkin Elmer Turbomass). GC-ECD for DeBDE determination used a short column (BPI 12 m x 0.22 mm ID x 0.1 (m film thickness) to reduce compound degradation and other PBDE oligomers were separated by GC/MS using a longer column (BP5 25 m x 0.22 mm ID x 0.25 (m film thickness) and detected using bromine ions 79 and 81 (Table 2).

3. Results

3.1 Partitioning of NPEOs and PBDEs to mixed liquor suspended solids at different sludge ages

With an increase in sludge age there is a concomitant increase in MLSS concentration and also a change in floc structure and in the nature of bacterial surfaces as different bacteria become dominant species. A range of MLSS (2.6-21.7 g l-1) concentrations were used to determine the relationship between partitioning and MLSS concentration for PBDEs. To achieve higher solids content, MLSS samples were centrifuged at 400 g for 10 minutes and the settled sludge used to achieve the required solids content, and for low solids MLSS samples were diluted with Husmann apparatus effluent. After shaking for 18 hours duplicate samples were taken. As the MLSS concentration increased the removal from the aqueous phase also increased with correlation in the range r2 = 0.97-0.99, with the exception of DeBDE with r2 = 0.92 (Fig. 2). The sorption to MLSS approximately doubled with doubling MLSS concentration with the exception of DeBDE where sorption increased exponentially (R2 = 0.98). However, the mass of PBDE compounds sorbed per unit mass of MLSS decreased with increasing MLSS concentrations as the available PBDE was reduced.

As the NPEO chain length increases and the oligomers become more hydrophilic, their adsorption was observed to decrease, and as the number of bromine atoms decreases in PBDEs they also become more hydrophilic and the partitioning decreased (Fig. 3). The compounds that accumulated onto the solid phase most rapidly were those least soluble in water and the most hydrophobic, such as NP and DeBDE.

3.2 The impact of hydraulic retention time on the rate of partitioning of APEOs and PBDEs to mixed liquor suspended solids

Samples were refrigerated at 4 oC for 30 minutes to inhibit biological activity and duplicate samples taken at intervals of approximately 1 hour for 6 hours. Chilling the samples at 4 oC inhibits almost completely biological activity ensuring biodegradation did not impact, so partitioning alone could be assessed.

Hydraulic retention time (HRT) is the amount of time the sewage spends in the aeration chamber during activated sludge treatment and is an important factor when considering whether bacteria will have a long enough exposure time to degrade or adsorb a compound. Log Kow correlated with the rates of partitioning for NPEOs and for PBDEs when compound concentrations were normalised for initial concentrations (Fig. 4). The rate of partitioning was also related to the concentration of compound available (Table 3). With higher initial concentrations the rate of partitioning increased.

As the system reached equilibrium the rate of partitioning decreased, for example, from 3.88 μg g-1 hr-1 to 0.08 μg g-1 hr-1 for BDE-154 and from 9.9 μg g-1 hr-1 to 0.57 μg g-1 hr-1 for DeBDE. The percentage reduction in partitioning rate decreased with increasing bromination from 98% for BDE-154 to 94% for DeBDE for example. Alkylphenolic compounds demonstrated the same pattern with an inverse relationship between the number of ethoxylate groups and the rate of partitioning.

3.3 The relationship between organic matter content and partitioning

Kom is the amount sorbed per unit weight of organic matter in the solid phase and as the organic carbon content has an impact on the sorption potential of floc, it should be considered in calculating the partition coefficient using

Kom = 100K / % MLVSS

Where K is calculated from

K = CML/ CAQ

Where CML is the compound concentration in the total MLSS and SAQ is that of the aqueous phase

The relationship between experimentally derived log Kom and calculated log Kow values is shown in figure 5 demonstrating the correlation (r2 = 0.92) between increasing log Kom with increasing log Kow for NPEO and PBDE compounds. This shows that the use of log Kom values would be more appropriate than Kow in models to evaluate removal of these compounds from wastewaters.

3.4 Freundlich isotherms for PBDE congeners

The partitioning behaviour of organic compounds can be described by the Freundlich isotherm which was calculated by plotting the log equilibrium concentration in the solid phase (log ML) against the log equilibrium concentration in the aqueous phase (log AQ)

log ML = log K + 1/n log AQ

where adsorption capacity is represented by k and adsorption constant by 1/n.

Using Freundlich isotherms the sorption constant was greater than 1 for each PBDE compound (Table 4). The low environmental concentrations used resulted in a linear isotherm as only a limited amount of the sorption capacity was utilsed.

Adsorption capacity generally increased and adsorption constant generally decreased with increasing log Kow. BDE-153 was the exception, however it is present in the DE-79 mixture at higher concentration and competitive binding cannot be ruled out. Pure standards would be required to accurately quantify Fruendlich coefficients individually and after this preliminary study purchasing the more costly pure compounds would be warranted.

4. Discussion

Compounds with a log Kow of less than 2.5 (Rogers, 1996), such as long chain NPEOs, exhibit minimal sorption potential and the major removal mechanism is likely to be degradation if compounds are susceptible. For compounds with log Kow values greater than 4, such as PBDEs, NP and short chain NPEOs, which are less susceptible to biodegradation, removal via association with solids will be the major removal mechanism due to their high sorption potential and the higher rate of sorption as demonstrated in this study.

At low (c, the high mass flows of wasted sludge and the wash-out of slow growing specialised degrading bacteria results in the major removal pathway being association with the solid phase, possibly as a result of high wastage resulting in high growth rates and rapid replenishment with new cells and relative abundance of unsaturated binding sites. Increasing the (c increases the MLSS concentration and reduces the amount of sludge wastage therefore results in a decrease in compound concentrations in the final effluent due to increased sorption and/or biodegradation by slower growing bacteria. Bacterial cells in the stationary phase of growth are more hydrophobic than those growing exponentially and sludge surfaces become more hydrophobic and less negatively charged with a higher sludge age (Liao et al., 2001) resulting in partitioning increasing with increasing (c due to changing properties and increased solids. Therefore, (c becomes an influential treatment process variable for more hydrophobic compounds such as PBDEs, short chain NPEOs and NP, whose predominant removal mechanism is through association with biological flocs. This is highlighted for PBDEs in this work as partitioning increases relative to increasing MLSS concentration and organic carbon content.

As the rate of removal generally correlates with the solids removal for hydrophobic, lipophilic compounds, if the concentration of effluent suspended solids is high it is probable that concentrations of EDC’s in effluent will be elevated, as compounds with high log Kow values will be associated with the non-settleable solids. A low (c leads to elevated effluent suspended solids and during the winter months when the temperature is lower the effluent suspended solids may be adversely affected with a concomitant impact on EDC removal (Langford and Lester, 2002).

The rate of sorption decreased with time for both groups of compounds which may be as a result of progressive saturation of sorbent binding sites and a reduction in available sorbate for binding as well as due to reaching equilibrium (Gao et al., 1998). This study indicates that a reduction in the rate of partitioning would make it difficult to ensure all traces of the compounds are removed from effluent with a typical HRT of 6-10 hours and result in some of the compounds entering the aquatic environment through effluent discharge.

In other work (John et al., 2000), adsorption partition coefficients correlated with organic carbon content. In addition to this, the current work highlights the relationship between log Kow with log Kom, and log Kow with the rate of partitioning demonstrating the importance of a compounds hydrophobic nature in determining its fate in wastewater treatment processes. Generally, the more hydrophobic and stable a compound the greater the amount accumulating in sludge (Meakins et al., 1994), which appears to be an inevitable removal pathway for compounds such as NP and PBDEs.

Competitive binding during wastewater treatment is a possibility due to the variety of organic compounds generally found in sludge. Other work also supports the possibility of competition effects looking at pesticides and estrogens in sediment (Gao et al., 1998; Lai et al., 2000; Scrimshaw and Lester, 1997). The effects of competitive binding increase with compound hydrophobicity (Lai et al., 2000) and could be useful in explaining the results for BDE-183 which is present in high concentrations in DE-79 but has shown results that do not correlate with other compounds in this study.

Due to the non-polar, hydrophobic nature of PBDEs, NP and short chain NPEOs it would seem that the majority of these compounds will be removed from the aqueous phase by sorption to solids suggesting that sedimentation will result in their accumulation in sludge and have implications for sludge disposal routes.

Conclusions

An increase in MLSS, as a result of operating at higher sludge ages results in an increased removal of the more hydrophobic PBDE congeners, NP and lower ethoxylates from the aqueous phase. Partitioning rates were demonstrated to be rapid, with 70% of NP binding within 10 minutes, although typical HRT for activated sludge processes would not allow for equilibrium conditions to occur. It was also found that the extent and rate of partitioning was proportional to Log Kow, with rapid initial uptake, which subsequently. It was also apparent that log Kow correlated with log Kom within compound groups.

#### Acknowledgements

One of the authors (KHL) is grateful to EPSRC and Anglian Water Plc. for research funding. All authors are grateful to EPSRC for the award of GR/N16358/01 without which this programme would not have been possible. The authors would also like to thank Colin Allchin of CEFAS, Burnham-on-Crouch, UK, for the donation of DE-79.

References

Ahel, M. and Giger, W., 1993. Partitioning of alkylphenols and alkylphenol polyethoxylates between water and organic solvents. Chemosphere 26, 1471-1478.

Allchin, C. R., Law, R. J. and Morris, S., 1999. Polybrominated diphenylethers in sediments and biota downstream of potential sources in the UK. Environ. Poll. 105, 197-207.

Blackburn, M. and Waldock, M., 1995. Concentrations of alkylphenols in rivers and estuaries in England and Wales. Water Res. 29, 861-869.

Desbrow, C., Routledge, E.J., Brighty, G.C., Sumpter, J.P., Waldock, M., 1998. Identification of estrogenic chemicals in STW effluent. 1. Chemical fractionation and in Vitro biological screening. Environ. Sci. Technol. 32, 1549-1558.

Dobbs, R. A., Wang, L. and Govind, R., 1989. Sorption of toxic organic compounds on waste water solids: Correlation with fundamental properties. Environ. Sci. Technol. 23, 1092-1097.

Ferguson, P. L., Iden, C. R. and Brownawell, B. J., 2000. Analysis of alkylphenol ethoxylate metabolites in the aquatic environment using liquid chromatography- electrospray mass spectrometry. Anal. Chem. 72, 4322-4330.

Gao, J. P., Maguhn, J., Spitzauer, P. and Kettrup, A., 1998. Sorption of pesticides in the sediment of the Teufelsweiher pond (Southern Germany). II: competitive adsorption, desorption of aged residues and effect of dissolved organic carbon. Water Res. 32, 2089-2094.

Garcia-Gutierrez, A. G., McIntyre, A. E., Perry, R. and Lester, J. N., 1982. The behaviour of PCBs in the primary sedimentation process of sewage treatment : A pilot plant study. Sci. Total Environ. 22, 243-252.

Gomes, J. and Lester, J. N., 2002. Endocrine Disrupters in Drinking Water and Water Re-use. In: Endocrine Disrupters in Wastewater and Sludge Treatment Processes. Birkett, J. W. and Lester, J. N. Florida, USA, CRC Press Ltd.

Guenther, K., Heinke, V., Thiele, B., Kleist, E., Prast, H. and Raecker, T., 2002. Endocrine Disrupting nonylphenols are ubiquitous in food. Environ. Sci. Technol. 36, 1676-1680.

Gustafsson, K., Bjork, M., Burreau, S. and Gilek, M., 1999. Bioaccumulation kinetics of brominated flame retardants (polybrominated diphenyl ethers) in blue mussels (Mytilus edulis). Environ. Toxicol. Chem. 18, 1218-1224.

HMSO, 1984. The conditionability, filterability, settlability and solids content of sludges. In: Methods for the Examination of Waters and Associated Materials, Standing Committee of Analysts.

John, D. M., House, W. A. and White, G. F., 2000. Environmental fate of nonylphenol ethoxylates: Differential adsorption of homologs to components of river sediment. Environ. Toxicol. Chem. 19, 293-300.

Lai, K. M., Johnson, K. L., Scrimshaw, M. D. and Lester, J. N., 2000. Binding of waterborne steroid estrogens to solid phases in river and estuarine systems. Environ. Sci. Technol. 34, 3890-3894.

Langford, K. H. and Lester, J. N., 2002. Fate and Behaviour of Endocrine Disrupters in Wastewater Treatment Processes. In: Endocrine Disrupters in Wastewater and Sludge Treatment Processes. Birkett, J. W. and Lester, J. N. Florida, USA, CRC Press.

Langford, K. H., Scrimshaw, M. D. and Lester, J. N. 2004. Analytical Methods for the Determination of Alkylphenolic Surfactants and Polybrominated Diphenyl Ethers in Wastewaters and Sewage Sludges. II Method Development. Environ. Technol. 25, 975-986.

Law, R. J., Allchin, C. R., Bennett, M. E., Morris, S. and Rogan, E., 2002. Polybrominated diphenyl ethers in two species of marine top predators from England and Wales. Chemosphere 46, 673-681.

Liao, B. Q., Allen, D. G., Droppo, I. G., Leppard, G. G. and Liss, S. N., 2001. Surface properties of sludge and their role in bioflocculation and settlability. Water Res. 35, 339-350.

McIntyre, A. E., Perry, R. and Lester, J. N., 1981. The behaviour of polychlorinated biphenyls and organochlorine insecticides in primary mechanical waste water treatment. Environ. Poll. (Series B) 2, 223-233.

Meakins, N. C., Bubb, J. M. and Lester, J. N., 1994. The fate and behaviour of organic micro pollutants during waste water treatment. Int. J. Environ. Poll. 4, 27-58.

Meerts, I. A. T. M., van Zanden, J. J., Luijks, E. A. C., van Leeuwen-Bol, I., Marsh, G., Jakobsson, E., Bergman, A. and Brouwer, A., 2000. Potent competitive interactions of some brominated flame retardants and related compounds with human transthyretin in vitro. Toxicol. Sci. 56, 95-104.

Öberg, K., Warman, K. and Öberg, T. 2002. Distribution and levels of brominated flame retardants in sewage sludge. Chemosphere 48, 805-809.

Rahman, F., Langford, K. H., Scrimshaw, M. D. and Lester, J.N. 2001. Polybrominated diphenyl ether (PBDE) flame retardants – a review. Sci Total Environ.275, 1-17.

Rogers, H. M., 1996. Sources, behaviour and fate of organic contaminants during sewage treatment and in sewage sludges. Sci. Total Environ. 185, 3-26.

Routledge, E. J. and Sumpter, J. P., 1996. Estrogenic activity of surfactants and some of their degradation products assessed using a recombinant yeast screen. Environ. Toxicol. Chem. 15, 241-248.

Scrimshaw, M. D. and Lester, J. N., 1997. Estimates of the inputs of polychlorinated biphenyls and organochlorine insecticides to the River Thames derived from the sediment record. Philosoph. Trans.: Math., Phys. Eng. Sci. 355, 189-212.

Scrimshaw, M. D., Langford, K. H. and Lester, J. N. 2004. Analytical Methods for the Determination of Alkylphenolic Surfactants and Polybrominated Diphenyl Ethers in Wastewaters and Sewage Sludges. I A Review of Methodologies. Environ. Technol. 25, 967-974.

Shang, D. Y., Ikonomou, M. G. and Macdonald, R. W., 1999. Quantitative determination of nonylphenol polyethoxylate surfactants in marine sediment using normal-phase liquid chromatography-electrospray mass spectrometry. J. Chrom. A 849, 467-482.

Stoveland, S. and Lester, J. N., 1980. A study of the factors which influence metal removal in the activated sludge process. Sci. Total Environ. 16, 37-54.

Tittlemier, S. A., Halldorson, T., Stern, G. A. and Tomy, G. T., 2002. Vapor pressures, aqueous solubilities, and Henry's Law constants of some brominated flame retardants. Environ. Toxicol. Chem. 21, 1804-1810.

USEPA, 2001. Estimation Program Interface (EPI) Suite, Version 3.10. Environmental Protection Agency, Washington DC, USA,

FIGURES

Fig. 1. Extraction methods for NP, NPEOs (A) and PBDEs (B)

Fig. 2. Partitioning of PBDEs with increasing MLSS concentration after 10 minutes equilibration time

Fig. 3. Partitioning of Igepal CO520 (A) and PBDEs (B) from aqueous phase to solid phase in MLSS (6.5 g l-1) after 10 minutes equilibration (white) and 7 hours equilibration (black).

Fig. 4. Correlation of rate of partitioning with Log Kow for A. PBDEs, and B. NPEOs. Normalised for compound mixture compositions.

Fig. 5. Laboratory derived partitioning to organic matter (log Kom) and calculated log Kow values  (calculated from USEPA EPI Suite program (USEPA, 2001) for PBDEs and calculated from literature for NPEOs (Ahel and Giger, 1993)).

Fig. 1. Extraction methods for NP, NPEOs (A) and PBDEs (B)

Fig. 2. Partitioning of PBDEs with increasing MLSS concentration after 10 minutes equilibration time

Fig. 3. Partitioning of Igepal CO520 (A) and PBDEs (B) from aqueous phase to solid phase in MLSS (6.5 g l-1) after 10 minutes equilibration (white) and 7 hours equilibration (black).

Fig. 4. Correlation of rate of partitioning with Log Kow for A. PBDEs, and B. NPEOs. Normalised for compound mixture compositions.

Fig. 5. Laboratory derived partitioning to organic matter (log Kom) and calculated log Kow values  (calculated from USEPA EPI Suite program (USEPA, 2001) for PBDEs and calculated from literature for NPEOs (Ahel and Giger, 1993)).

Table 1. Physico-chemcial properties of alkylphenolic compounds and polybrominated diphenyl ethers a(Langford and Lester, 2002), b(Tittlemier et al., 2002)

Table 2. Analysis of NP, NPEOs and PBDEs

Table 3. Partitioning rates of NPEOs and PBDEs in relation to spiking concentrations

|  | Initial concentration ((g l-1) | Initial partitioning rate (at 10 mins) ((g g-1 hr-1) | Final partitioning rate (at 5 hours) ((g g-1 hr-1) |
| --- | --- | --- | --- |
| PBDE |  |  |  |
| BDE-183 | 189 | 136 | 3.7 |
| BDE-153 | 47.4 | 37 | 0.96 |
| DeBDE | 30 | 9.9 | 0.57 |
| OcBDE | 8 | 7.84 | 0.4 |
| BDE-154 | 6 | 3.88 | 0.08 |
| Surfactants |  |  |  |
| NP | 300 | 1.84 | 0.004 |
| NP3EO | 60 | 0.36 | 0.008 |
| NP5EO | 54 | 0.026 | 0.001 |
| NP6EO | 51 | 0.008 | 0.0002 |
| NP8EO | 18 | 0.0046 | 0.00017 |
| NP9EO | 12 | 0.0023 | 0.00013 |
| NP10EO | 6 | 0.0011 | 0.000058 |
| NP2EO | 4.2 | 0.4 | 0.006 |

Table 4. Adsorption capacities and adsorption efficiencies derived from Freundlich isotherms for PBDEs compared to Log Kow values

| PBDE Congener | Log Kow | sorption coefficient (log k) | sorption constant (1/n) |
| --- | --- | --- | --- |
| Deca | 12.8 | 12.94 | 2.5 |
| Octa 1 | 10.3 | 10.34 | 2.4 |
| Octa 2 | 10.3 | 9.42 | 3 |
| Octa 3 | 10.3 | 9.33 | 3 |
| BDE-153 | 9.4 | 5.4 | 4.2 |
| BDE-183 | 8.5 | 2.02 | 5.5 |
| BDE-154 | 8 | 10.38 | 2.17 |